## Slide 1: Underlying Technologies

## Slide 2
2.1 Wired LANs
A Wired LAN (Local Area Network) is a network where computers and devices are connected using physical cables (mostly twisted-pair or fiber optic cables). It provides high speed, reliability, and security for communication within a limited area like a building, campus, or office.
2.1.1 IEEE Standards (802.3)
IEEE 802.3 is a collection of standards that define the physical and data link layers for wired Ethernet LANs, mainly focusing on media access control (MAC) with carrier-sense multiple access with collision detection (CSMA/CD). It covers a wide range of Ethernet technologies that use copper or fiber optic cables to interconnect devices like switches, routers, and computers within a network.

## Slide 3
2.1.2 Ethernet Frame Format
The Ethernet frame format comprises several fields:
Preamble (7 bytes): Synchronizes sender and receiver clocks.
Start Frame Delimiter (SFD) (1 byte): Marks the start of the frame payload.
Destination MAC Address (6 bytes): Identifies the receiver device.
Source MAC Address (6 bytes): Identifies the sender device.
Ether Type/Length (2 bytes): Indicates the type of payload or its length.
Payload (46–1500 bytes): Actual transmitted data.
Frame Check Sequence (FCS) (4 bytes): Error detection mechanism.
2.1.3 Addressing
Ethernet uses MAC (Media Access Control) addresses for communication.
A MAC address is a 48-bit (6 bytes) unique address assigned to each network interface card (NIC).
It is written in hexadecimal format (e.g., 00:A1:B2:C3:D4:E5).
There are two types of addressing:
  Unicast: One-to-one communication
  Broadcast: One-to-all communication
  Multicast: One-to-many (specific group)

## Slide 4
Type | Speed | Medium | Typical Use case | Coverage | Features
Standard Ethernet | 10 Mbps | Coaxial/UTP/Fiber | Legacy LAN connections | Up to 500m | Simple, cost-effective
Fast Ethernet | 100 Mbps | Twisted Pair/Fiber | Small business/home offices | Up to 10km | Easy upgrade from 10Mbps
Gigabit Ethernet | 1 Gbps | Twisted Pair/Fiber | High-speed enterprise/home | Up to 70km | High bandwidth
Ten Gigabit Ethernet | 10 Gbps | Twisted Pair/Fiber | Data centers, backbone networks | Varies, much higher | Highest performance
Standard Ethernet (IEEE 802.3, 10 Mbps): Used with thick/thin coaxial, unshielded twisted pair (UTP), or Fiber cables.​
Fast Ethernet (IEEE 802.3u, 100 Mbps): Simple configuration, popular for small and medium networks.​
Gigabit Ethernet (IEEE 802.3ab/802.3z, 1 Gbps): Used in high-speed and large networks, requires higher grade cables and devices.​
Ten Gigabit Ethernet (IEEE 802.3ae, 10 Gbps): For backbone and data center networks, provides very high bandwidth
2.1.4 Standard Ethernet, Fast Ethernet, Gigabit Ethernet, Ten-Gigabit Ethernet

## Slide 5
2.1.5 Fiber Optic LAN
Fiber optic LANs use optical fiber cables for network connectivity, providing very high data rates, long distance coverage, minimal signal loss, and immunity to electromagnetic interference. These networks are preferred in modern large enterprises, campuses, and industrial sites due to their speed, reliability, and security. Fiber optic cables are also scalable, supporting transmission speeds up to hundreds of gigabits per second.​
2.2 Wireless LANs
A Wireless LAN (WLAN) connects devices through radio waves instead of cables. It allows users to move freely within the network coverage area while maintaining a network connection. WLANs are commonly used in homes, offices, colleges, and public places (Wi-Fi hotspots).

## Slide 6
2.2.1 IEEE 802.11 (Wi-Fi)
IEEE 802.11 is a series of standards for wireless LANs (WLANs), designed to enable high-speed wireless networking in the 2.4 GHz, 5 GHz, and newer 6 GHz bands. It specifies both the physical layer (signal transmission and frequency) and MAC layer protocols, ensuring interoperability among different devices and manufacturer
2.2.2 IEEE 802.11 Extensions: b/a/g/n/ac/ax/be/bn
Extension | Frequency | Max Data Rate | Notable Features
802.11b | 2.4 GHz | 11 Mbps | First widespread consumer Wi-Fi, simple, robust
802.11a | 5 GHz | 54 Mbps | Less crowded band, higher speed, shorter range
802.11g | 2.4 GHz | 54 Mbps | Combines b/g compatibility, better speed
802.11n | 2.4/5 GHz | 600 Mbps | MIMO, channel bonding
802.11ac | 5 GHz | up to 7 Gbps | Wider channels, MU-MIMO, Wi-Fi 5
802.11ax | 2.4/5/6 GHz | 9.6 Gbps | Wi-Fi 6/6E, OFDMA, more devices, improved efficiency
802.11be, bn | 6 GHz | Multi-Gbps | Newest, future standards for ultra-high throughput, advanced multiplexing

## Slide 7
2.2.3 MAC Sublayer
The 802.11 MAC sublayer manages access to the wireless medium, dealing with frame encapsulation, address management, error detection, and media arbitration. It supports two key modes:
Distributed Coordination Function (DCF): Uses CSMA/CA for asynchronous data.
Point Coordination Function (PCF): Provides centralized, time-bounded service using polling.​ MAC frame fields include Frame Control, Duration, Address fields, Sequence, Data, and Check Sequence, supporting multiple communication types
2.2.4 Addressing
Unlike Ethernet (with source/destination), 802.11 frames often use up to four address fields:
Address 1: Receiver Address (RA)
Address 2: Transmitter Address (TA)
Address 3: Destination Address (DA) or Source Address (SA, depending on traffic direction)
Address 4: Used for mesh or WDS scenarios This complexity covers wireless clients, APs, and the final target device on the network, enabling varied forwarding and bridging models.

## Slide 8
2.2.5 Bluetooth and Wi-Fi Direct
Feature | Bluetooth | Wi-Fi Direct
Typical Speed | 3 Mbps | Up to several Gbps
Range | ~50 meters (Class 2), up to 300 m (Class 1) | ~200 meters
Use | Low-power PANs, peripherals | Direct high-speed device-to-device connection, no AP needed
Power Consumption | Low | Higher
Data Handling | Small data bursts (audio, sensors) | Large files, streaming video
Security | Sufficient, but less robust | WPA/WPA2/WPA3 support

## Slide 9
Bluetooth
Defined by the IEEE 802.15.1 standard.
Short-range wireless technology (up to 10 m).
Used for connecting peripherals like headphones, keyboards, phones, etc.
Operates at 2.4 GHz using Frequency Hopping Spread Spectrum (FHSS).
Forms a Piconet (one master and up to seven slaves).
Wi-Fi Direct
A technology that allows two Wi-Fi devices to connect directly without a router or access point.
Similar to Bluetooth but provides higher speed and range.
Commonly used for file transfer, printing, and device-to-device sharing.