## Slide 1: 8051 Instruction set and Programming

## Slide 2
2.1 Instruction set
Data Transfer Instruction
Arithmetic Instruction
Logical Instruction
Branching Instruction
Machine control Instruction
Boolean Instruction
Data Transfer Instruction :- this instruction are use to transfer the data from the source operand to the destination operand
1. MOV : used to copy the byte or word
e.g. Mov A, #03H
2. PPUSH: Used to put a word at the top of the stack.
e.g. PPUSH RI, R2
3. POP : Used to get a word from the top of the stack to the provided location
e.g. POP RO
4. PUSH A : Used to get words from the stack to all registers
e.g. PUSH A ;

## Slide 3
5. POP A : Used t get words from the stack to all registers
e.g. POP A
6. XCHG : Used to exchange the data from two location.
e.g. XCHG AX, BX
2. Arithmetic Instruction : These Instruction are used to perform Arithmetic operations like Addition , Subtraction , Multiplication , division , etc.
ADD : Used to add provided byte to byte / word to word
USB : Used to subtract the byte from byte / word form word
Mul : Used to Multiply unsigned byte by byte / word by word
DIV : Used to divide the unsigned byte by byte or unsigned double word by word
INC : Used to increment the provided byte / word by 1
DEC : Used to decrement the provided byte / word by 1
3. Logical Instruction : These instruction are used to perform operations where data bits are involved
XOR : Used to Exclusive – OR operation over each bit in a byte / word with the corresponding bit in another byte / word
AND : Used for adding each bit in a byte / word with the corresponding bit in another byte / word
OR : Used to multiply each bit in a byte / word with the corresponding bit in another byte / word

## Slide 4
4. NOT : used to invert each bit of a byte or word
5. TEST : Used to add operands to update flags , without affection operands
4. Branching Instruction : These instruction are used to transfer / branch the instruction during an execution
CALL : Used to call a procedure and save their return address to the stack (ACALL and LCALL)
JMP : Used to jump to the provided address to proceed to the next instruction
1. Unconditional Jump :
SJMP (Short Jump) – 256 byte we can use this instruction t half the program
LJMP (Long Jump) – 2k byte It can Jump to symbolic label
AJMP (Absolut Jump ) – 64 kb performed inside page only
2. Condition JUMP :
JC – Jump if carry flag is 1
JNC – jump of carry flag is 0
JZ – Jump if zero flag is 1
JNZ – Jump if zero flag is 0
JB – Jump if bit is 1
JNB – Jump of bit is 0

## Slide 5
5. Machin control Instructions : These instruction are used to control the action by setting / Resetting the flag value
STC : set carry flag , set = 1
CLC : Clear carry flag , clear = 0
CMC : Complement at the state of carry flag
HLT : Stop the execution
WAIT : It is used to synchronize 8051 , with peripheral devices
LOCK : Used to lock entire physical memory space
NOP : NO Operation
6. Boolean Instruction : This grow of instruction is associated with the single bit operation of the 8051
CLR : clear a bit or cy flag
e.g. CLR P1 .1
CLR C
2. SET B : set a bit or cy flag
e.g. SETB p2 . 1
SETB C
3.CPL : Complement a bit or cy flag
e.g. CPL 45 H
4. ORL / ANC : ORL / ANC a bit with the cy flag
e.g. ORL c , 20H or bit 20 of bitt addressable memory with the cy flag
e.g. ANC C , 34H

## Slide 6
2.2 Addressing modes
1] Immediate addressing mode
2] Direct addressing mode
3] Register addressing mode
4] Register indirect addressing mode
5] Indexed addressing mode
6] Implied addressing mode
1] Immediate addressing mode
In this addressing mode the source operand is constant
Immediate data must be proceeded by the sign (#) This addressing mode can be used to load information into any of the register
e.g. MOV A , # 35 H; load 35H into A
MOV R3 , # 63H; load into R3
MOV DPTR , # 521 H ; load 521H into DPTR
2] Direct Addressing mode
This mode is used to access RAM location (30 – TF H)
e.g. MOV R0 , 44H
MOV A , R4
MOV 56 H, A

## Slide 7
3] Register Addressing mode :
Register addressing mode involve the use of register to hold the data to be manipulated
e.g. MOV R2, A ; copy the content of A into R2
MOV R1, A ; copy the content of A into R1
MOV A, R3; copy the content of R3 into A
4] Register indirect addressing mode :
In this mode , register is used as pointer to the data In this mode only register (R0 and R1) are used
e.g. MOV A, @R1
MOV @ R0,R1
ADD A, @R0
5] Indexed addressing mode :
This mode is used in accessing data element of look up table entries location in program code ROM of 8051
e.g. MOV A, @ A + DPTR
MOV A, @ A + PC
6] Implied addressing mode :
There will be single operand these types of instruction work on specific register only . Also known as register specific instruction
e.g. RLA:

## Slide 8
2.3 Assembly language programming
Assembly language program for Addition , multiplication , subtraction , division
ORG 0000H ; Program start address
; Addition
MOV A, #03H ; Move immediate data 03h into accumulator A
ADD A, #04H ; Add immediate data 04h to accumulator A
MOV R0, A ; Store result in register R0
; Subtraction
CLR A ; Clear accumulator A
CLR C ; Clear carry flag
MOV A, #05H ; Move immediate data 05h into accumulator A
SUBB A, #02H ; Subtract immediate data 02h with borrow from accumulator A
MOV R1, A ; Store result in register R1

## Slide 9
; Multiplication
CLR A ; Clear accumulator A
MOV A, #03H ; Move immediate data 03h into accumulator A
MOV B, #04H ; Move immediate data 04h into register B
MUL AB ; Multiply A by B, result in B (MSB), A (LSB)
MOV R2, A ; Store lower 8 bits of result in R2
MOV R3, B ; Store upper 8 bits of result in R3
; Division
CLR A ; Clear accumulator A
MOV A, #95H ; Move immediate data 95h into accumulator A (dividend)
MOV B, #10H ; Move immediate data 10h into register B (divisor)
DIV AB ; Divide A by B, quotient in A, remainder in B
MOV R4, A ; Store quotient in R4
MOV R5, B ; Store remainder in R5
END ; End of program

## Slide 10
Assembly language Program of find largest number from given data bytes!
ORG 0000H ; Program start address
MOV R0, #40H ; Initialize R0 with starting memory address 40H
MOV R1, #05H ; Initialize R1 with count of 5 (number of data bytes)
MOV A, #0FFH ; Initialize accumulator A with 0FFH (assuming max value start)
DOWN:
MOV B, @R0 ; Move data at address pointed by R0 into B
CJNE A, B, VP ; Compare A and B, jump to VP if not equal
UP:
JNC A_LARGE ; If carry flag not set (A >= B), jump to A_LARGE
MOV A, B ; Else move B into A (B is larger)
A_LARGE:
INC R0 ; Increment R0 to point to next data byte
DJNZ R1, DOWN ; Decrement R1 and loop until zero
MOV 50H, A ; Store the largest number found at memory address 50H
SJMP $ ; Infinite loop to stop program
END

## Slide 11
Assembly language Program for Ascending order:
ORG 0000H
MOV R0, #05H ; Initialize pass counter (n-1 passes for n elements)
MOV DPTR, #3000H ; Initialize memory pointer (array start address)
MOV R1, #05H ; Initialize byte counter
PASS: MOV R2, DPTR ; Save the lower byte address (array pointer)
MOV A, @DPTR ; Read first number from array into Accumulator
MOV 40H, A ; Transfer the number into temp memory (B register substitute)
INC DPTR ; Increment memory pointer
MOV A, @DPTR ; Read next number from array into Accumulator
CJNE A, 40H, COMPARE ; Compare with temp (previous) number
SKIP: INC DPTR ; Move to next element
DJNZ R1, PASS1 ; Byte counter loop
DJNZ R0, PASS ; Pass counter loop
SJMP END

## Slide 12
COMPARE:
JNC SKIP ; If current >= previous, skip
MOV DPL, R2 ; Else exchange
MOVX A, @DPTR
MOVX @DPTR, 40H
MOVX @R2, A
SJMP SKIP
PASS1: ; Loop within pass
END: SJMP END

## Slide 13
Assembly language program for Descending order:
ORG 0000H
MOV RO, #05H
UP1: MOV DPTR, # 3000H
MOV R1, HO4H
UP: MOV R2, D P L
MOVX A, @DPTR
MOV OFOH, A
INC DDTR
MOVX A @DPTR
CJNE A, OFOH, DN
AJMP SKIP
DN: JC SKIP
MOV DPL, R2
MOVX @DPTR, A
INC DPTR
MOV A, OFOH
MOVX @DPTR, A
SKIP: DJNZ R1, UP
DJNZ PO, UP1
END

## Slide 14
2.4 8051 programming in C
8051 programming in C refers to writing embedded software for the 8051 microcontroller using the C language instead of assembly. This improves readability, maintainability, and speeds up development compared to pure assembly programming.​
Introduction to 8051 C Programming
The 8051 microcontroller can be programmed using Embedded C, which allows direct control of I/O ports, timers, and serial communication using high-level syntax.​
Most modern 8051 development environments (such as Keil C51) support standard C syntax with some hardware-specific extensions.
Basic Structure of an 8051 C Program
#include <reg51.h> // Header file specific to 8051
void main(void) {
P1 = 0xFF; // Turn ON all bits of Port 1
while (1); // Infinite loop
}

## Slide 15
Header files like <reg51.h> define register maps for SFRs and peripherals.​
Ports (P0, P1, P2, P3) can be accessed using simple assignment statements.
Common Operations
Blinking an LED
#include <reg51.h>
void MSDelay(unsigned int);
void main() {
while(1) {
P1 = 0x55; // Output pattern to Port 1
MSDelay(250);
P1 = 0xAA; // Alternate pattern
MSDelay(250);
}
}
void MSDelay(unsigned int itime) {
unsigned int i, j;
for (i = 0; i < itime; i++)
for (j = 0; j < 1275; j++);
}
This example toggles the bits of Port 1 with a delay.

## Slide 16
2. Reading from a Port and Writing to Another
#include <reg51.h>
void MSDelay(unsigned int);
void main() {
unsigned char d;
P1 = 0xFF; // Set P1 as input
while(1) {
d = P1; // Read from P1
MSDelay(500);
P2 = d; // Output to P2
}
}
Data is read from Port 1 and then output to Port 2 after a delay.​